## Slide 1
RuggedBoard
ADC
https://community.ruggedboard.com

## Slide 2
RB-ADC
The main purpose of the Industrial I/O subsystem (IIO) is to provide support for devices that in some sense perform either analog-to-digital conversion (ADC) or digital-to-analog conversion (DAC) or both.
Devices that fall into this category include:
analog to digital converters (ADCs)
accelerometers
capacitance to digital converters (CDCs)
digital to analog converters (DACs)
gyroscopes
inertial measurement units (IMUs)
color and light sensors
magnetometers
pressure sensors
proximity sensors
temperature sensors

## Slide 3
RB-ADC
Software triggers are an ADC operating mode where the software starts the conversion.
This feature is exposed by IIO through the following files:
in_voltageX_raw: raw value of the channel X of the ADC
in_voltage_scale: value you have to multiply in_voltageX_raw with to have a value in microvolts
Note: Reading into in_voltageX_raw will perform a software trigger on the ADC, then block until the conversion is completed, and finally return the value of this conversion.

## Slide 4
RB-ADC
root@rugged-board-a5d2x-sd1:~#cat /sys/bus/iio/devices/iio\:device0/in_voltage0_raw
4095
Here is the output on the RBA5D2X console that shows an ADC measure when a 3.3V DC power supply is connected between analog ground GND and ADC input in mikrobus pins
root@rugged-board-a5d2x-sd1:~#cat /sys/bus/iio/devices/iio\:device0/in_voltage_scale
0.805664062 ​
We can calculate the result:
4095 x 0.805664062 = 3299.19433389 mv
= 3.29 v

## Slide 5
RB-ADC
Connect poteniometer in analog pin of mikrobus and vary the potentiometer calculate the resultant voltage manually and using C program.

## Slide 6
Connect-us
Developer
Wiki

## Slide 7
Open Discussions