## Slide 1
Rugged Board
PWM
https://community.ruggedboard.com

## Slide 2
RB-PWM
PWM in Rugged Board through sysfs
Using pwmchip interface
pwmchip0 is used for PWM interface
List of files in pwmchip0
Note: npwm gives number of pwm channels

## Slide 3
RB-PWM
echo x > /sys/class/pwm/pwmchip0/export
where x takes value 0,1,2,3
pwm1 is present in mikro bus we are going to use this for our experiment

## Slide 4
RB-PWM
pwm1
enable
period
duty_cycle

## Slide 5
RB-PWM
# cd /sys/class/pwm/pwmchip0/
# echo 1 > export
# echo 100 > /sys/class/pwm/pwmchip0/pwm1/period
# echo 0.25 > /sys/class/pwm/pwmchip0/pwm1/duty_cycle
# echo 1 > /sys/class/pwm/pwmchip0/pwm1/enable
Step1: export pwm1
Step2: set period for pwm1
Step3: set duty_cycle for pwm1
Step4: enable pwm1

## Slide 6
RB-GPIO
C program to change the brightness of the LED

## Slide 7
Open Discussions

## Slide 8
Connect-us
Developer
Wiki